## Slide 1
This is the neutron volumetric spectrum that SOURCES 4A (mod) predicts for Copper with 1 ppb Th contamination.
I want to use this to find out how many primary decays (from 232Th) it takes to create 1 neutron.
Producing 1 neutron in the Cu volumes of SuperCDMS will obviously not amount to many registered interactions in the detectors. Many will not hit the detectors at all. However, we could test this by creating a volumetric neutron source in the Cu of SuperSim.

## Slide 2
Integrating this spectrum, I get a total volumetric source rate of 1.81x10-10 neutrons/s/cm3/ppb.
NB: In one year, 1 ppb contamination is equivalent to 0.0057 neutrons/cm3. Equivalently, this corresponds to 175 years to get 1 neutron in each cm3.
Remember, this is for 1 ppb of Th contamination. It is likely we have a lot more than this. However, in a simulation, to get meaningful background distributions we certainly need many counts. So, if I calculate how many decays it takes to get 1 neutron, that will be a benchmark because if we simulated the neutrons as a volumetric source, there would be a neutron for every primary simulated event.
I will calculate it like this (the bottom number is just the number above in bold):
Number of decays /s/cm3/1ppb
Number of produced neutrons /s/cm3/1ppb

## Slide 3
Probably, the way one would simulate the Th progeny in Geant4 is to place a 232Th atom in the contaminated material at a random location, and, let it decay. All the subsequent daughter decays will be captured in that event, no matter what the half life.
In practice, the a-decays further down the chain will happen at the same rate as the Th decay, assuming secular equilibrium. That means for each Th decay there are a handful of a-decays, each with the possibility of creating a neutron by the (a,n) process.
The half life for 232Th is 1.41x1010 y, see left from nndc.bnl.gov

## Slide 4
First, we want to find out how many Cu atoms per cm3 and then use 1 ppb to find the total number of Th atoms per cm3 per ppb. Given that, we can use the decay equation to compute the denominator on the previous page.
1 amu is 1.674x10-24 g – I looked that up – it’s based on carbon atoms being exactly 12 amu. So, the density of Cu is 5.35x1024 amu/cm3.
A copper atom is 63.5 amu. The number density of room temp. copper is therefore: 9.99x1022 atoms/cm3.

## Slide 5
Based on the density of Cu, and the level of 1 ppb, the number of Th atoms present in copper is 9.99x1013 atoms/cm3/ppb.
Then, we can calculate the number of decays in a certain time from the radioactivity equation.
is the number of deays, is the original number of Th, and is the current number of Th. The radioactive law says:
Or, putting it together:

## Slide 6
For 1 yr the exponential factor in the parentheses is 4.92x10-11. That gives 4,911 decays /year/cm3/ppb.
Converting to per second gives: 1.56x10-4 decays /s/cm3/ppb
So, we can apply it to the equation:
Number of decays /s/cm3/1ppb
Number of produced neutrons /s/cm3/1ppb
1.56x10-4 decays /s/cm3/ppb
1.81x10-10 neutrons/s/cm3/ppb
And get: 861,878 decays/neutron

## Slide 7
Spontaneous fission is also a contributor to neutrons. Th has very little S.F. but 238U has a lot more (see left, branching of 5.4x10-5 % compare with ~10-9 % for Th).
In fact, our radiogenics are probably dominated by spontaneous fission of 238U. This could be simulated natively in SuperSim as well, if G4 has accurate S.F. simulation. I want to estimate how many decays we need for this one.

## Slide 8
Integrating this spectrum for 238U S.F., I get a total volumetric source rate of 3.41x10-9 neutrons/s/cm3/ppb.
The same calculation as before: based on the density of Cu, and the level of 1 ppb, the number of 238U atoms present in copper is 9.99x1013 atoms/cm3/ppb.
But now we got to use the halflife of 238U.
For 1 yr the exponential factor in the parentheses is 1.55x10-10.
That gives 15,526 decays /yr/cm3/ppb, but S.F. is only 5.44x10-5 % , so that is 8.4 S.F. /yr/cm3/ppb. Or:
2.68x10-10 S.F. /s/cm3/ppb

## Slide 9
So, we can apply it to the equation:
Number of S.F. /s/cm3/1ppb
Number of produced neutrons /s/cm3/1ppb
2.68x10-10 S.F. /s/cm3/ppb
3.41x10-9 neutrons/s/cm3/ppb
And get: 0.079 S.F./neutron or around 12.7 neutrons/S.F.
This number is much more feasible than the (a,n). We might in this case worry, however, that S.F. in G4 is modelled correctly—especially the correlations in neutrons emitted.